## Slide 1: Hardware Security

## Slide 2: AES-256 Encryption Wrapper with Multiple Modes
Χρηστοσ kαλλιγκατσησ 02526
Χρηστοσ θεοδοσιαδης 02393

## Slide 3: Abstract
This presentation describes the design and implementation of an AES-256 encryption wrapper module based on an AES-256 core sourced from OpenCores. The wrapper processes 180-bit input data by utilizing the core twice per encryption, padding the input for the second operation as required. It incorporates three modes of operation: Cipher Feedback Mode (CFB), Output Feedback Mode (OFB), and Counter Mode (CTR).

## Slide 4: Challenges and Objectives
Challenges:
- Handling 180-bit input with a 128-bit core
- Timing issues resolved using control flags
- Resource constraints on the Nexys A7 board
- Power constraints due to high dynamic power consumption
- Virtual implementation using Vivado
Objectives:
- Design a 180-bit AES encryption wrapper
- Support CFB, OFB, and CTR modes
- Validate through simulation and testing.

## Slide 5: AES Encryption Fundamentals
AES is a symmetric block cipher that encrypts/decrypts data in 128-bit blocks using a substitution-permutation network.
Main Steps:
- SubBytes
- ShiftRows
- MixColumns
- AddRoundKey
Key Lengths:
- AES-128: 10 rounds
- AES-192: 12 rounds
- AES-256: 14 rounds

## Slide 6: Advantages of 256-bit Key Length
- Enhanced security against brute-force attacks
- Greater resistance to future cryptanalysis (e.g., quantum computing)
- Compliance with high-security standards (e.g., government, financial institutions).

## Slide 7: Wrapper Module Design
- Input: 180-bit data, 256-bit key, 128-bit IV, mode control signal
- Output: 180-bit encrypted data
- Padding: Zero padding for 52-bit segment
- Sequential processing using a single AES core.

## Slide 8: Modes of Operation
- Cipher Feedback Mode (CFB): XOR plaintext with AES-encrypted IV
- Output Feedback Mode (OFB): Generate keystream from AES-encrypted IV
- Counter Mode (CTR): XOR plaintext with keystream from AES-encrypted counter.

## Slide 9: Simulation Results
Behavioral simulation in Vivado:
- CFB Mode: 1000ns, CPU = 18s, Elapsed = 2m16s, Memory = 3242 MB
- OFB Mode: 1000ns, CPU = 14s, Elapsed = 1m54s, Memory = 3249 MB
- CTR Mode: 1000ns, CPU = 17s, Elapsed = 2m08s, Memory = 3249 MB

## Slide 10: Implementation Details
- Modified AES-256 core for iterative encryption
- Added control signals (e.g., done_flag) for synchronization
- Utilized key expansion modules and S-boxes for compliance
- Tested with comprehensive testbench in Vivado.

## Slide 11: Challenges and Recommendations
Challenges:
- High power consumption
- Resource constraints on FPGA
- Timing and synchronization in iterative processing
Recommendations:
- Optimize design for power efficiency

## Slide 12: Conclusion
The AES-256 wrapper module supports secure 180-bit encryption with CFB, OFB, and CTR modes. Validated via behavioral simulation, the design meets objectives but requires optimization for power and resource efficiency.